## Slide 1: Working with the Intel 8080/8085 assembly Language

## Slide 2
Outline
Planned register usage:
REG B will hold operand 2 (control)
REG C will hold the bit mask
REGS DE will hold Operand 1 that cab shift to 16-bits
REGs HL will hold the 16-bit sum
In Memory:
100 is the address of Operand 1
102 is the address of Operand 2
104 & 105 is where the 16-bit product is to be stored
Load address of operand 1 into HL
Load operand 1 into register E
Zero Register D
move 1 into Reg C for the mask
Load address of Operand 2 into HL
Load Operand 2 into register B
Zero REGs HL for summing

## Slide 3
Now we test, add, and shift
1) Move REB B to REG A
AND with REG C (Mask)
Branch if zero to 2)
DAD (Double add DE to HL)
## Now shift Operand 1 in REGs DE
## Rotate REG C (Mask) left through Carry bit
## Branch if no carry back to 1)
2) MOV REG E to REG A
Clear carry bit
Rotate left through carry
Move REG A back to REG E
Move REG D to REG A
Rotate left through carry
Move REG A back to REG D
Move Reg C to A
Clear carry bit
Rotate REG A left through carry
Move REG A to REG C
Branch if no carry to 1)
Store REGs HL in memory
Halt

## Slide 4
In Memory:
100 is the address of Operand 1
102 is the address of Operand 2
104 & 105 is where the 16-bit product is to be stored
Load address of operand 1 into HL
LXI H, 100
Load operand 1 into register E
MOV E,M
Zero Register D
MVI D,0
move 1 into Reg C for the mask
MVI C,1
Load address of Operand 2 into HL
LXI H,102
Load Operand 2 into register B
MOV B,M
Zero REGs HL for summing
LXI H,0

## Slide 5
## Now we test, add, and shift
Move REB B to REG A
  MOV A,B
AND with REG C (Mask)
ANA C
Branch if zero to 2)
JZ 2)
DAD (Double add DE to HL)
DAD
## Now shift Operand 1 in REGs DE
## Rotate REG C (Mask) left through Carry bit
## Branch if no carry back to 1)
2) ## MOV REG E to REG A
MOV A,E
## Clear carry bit by setting to 1 and then complement
STC
CMC
## Rotate left through carry
RAL

## Slide 6
## Move REG A back to REG E
MOV E,A
## Move REG D to REG A
MOV A,D
## Rotate left through carry
RAL
## Move REG A back to REG D
MOV D,A
## Move Reg C to A
MOV A,C
## Clear carry bit
STC
CMC
## Rotate REG A left through carry
RAL
## Move REG A to REG C
MOV C,A
## Branch if no carry to 1)
JNC 1)
## Store REGs HL in memory
????????????
HLT
Homework:
Come up with a sequence of 8080/8085 assembly language instructions that will store the contents of register pair HL into memory locations 104 and 105. This is the 16-bit result of multiplying two 8-bit numbers together.
Due Wednesday October 21.